## Slide 1: Evaluating Congestion Control for Interactive Real-time Media
draft-singh-rmcat-cc-eval-03
IETF 87, RMCAT
Varun Singh, Joerg Ott

## Slide 2: Changes since -02
Cleanup of metrics
  There are still many OPEN ISSUES
Added RTP log format
Added a new guidelines
  Startup behaviour
Example Evaluation Scenarios section replaced by Evaluation Parameters
  Components to build new scenarios
Added Michael Romalho’s scenario proposal as an appendix
  Discussed in design team meetings
  Acknowledged Michael in the Contributors Section.

## Slide 3: Unfairness Metric
Instead of defining fairness, there has been discussion on defining "unfairness". The criteria are:
Do not trigger the circuit breaker.
Over 3 times or less than 1/3 times the throughput for an RMCAT media stream compared to identical RMCAT streams competing on a bottleneck, for a case when the competing streams have similar RTTs.
Over 3 times delay compared to RTT measurements performed before starting the RMCAT flow or for the case when competing with identical RMCAT streams having similar RTTs.
Does the criteria capture Unfairness adequately?

## Slide 4: Metrics: Open Issues
Define Unfairness
Define convergence time
  Related to Startup behaviour
Remove Bandwidth Utilization?
Remove Application trade-off?
  How to measure Throughput vs. Delay vs. Loss
  Or delegate this to the description of each scenario?

## Slide 5: Evaluation parameters
A suite of options to create new scenarios
List of Traffic Flows
List of Access Links
Link parameters
  List of link losses and link latency
List of Router queue lengths
  Droptail queue
List of Media flow parameters
Missing: TCP Cross-traffic parameters

## Slide 6: List of Traffic Flows
A single RMCAT flow by itself.
Competing with similar RMCAT flows. These competing flows may use the same algorithm or another candidate RMCAT algorithm.
Compete with long-lived TCP.
Compete with bursty TCP.
Compete with LEDBAT flows.
Compete with unresponsive interactive media flows (i.e., not only CBR).

## Slide 7: Parameters: Open Issues
Map wireless access links to link properties?
Losses
  Traces?
  Gilbert-elliot model?
Latency parameter guideline for a scenario:
  Hop-by-hop, or
  End-to-end