## Slide 1: Evaluating Congestion Control for Interactive Real-time Media
draft-singh-rmcat-cc-eval-00
8. November 2012
Varun Singh, Joerg Ott

## Slide 2: Current Status
Draft-01 makes some changes based on the list discussion
Main Open Issue: Quality Metric
  To analyse the trade-off between loss, throughput and delay.
  List discussion indicates against having it
Notes: Quality per bit (PSNR, SSIM, visual comparison)

## Slide 3: Metrics
Bandwidth Utilization = sending rate/capacity
  Under utilization
  Overuse
  Steady-state
Packet loss and discard rate
Fair share with similar flows
  Should be equal?
Fair share [open issue]
  Long TCP flows
  Short TCP flows
  Many and few competing flows
Measure: min, max, average for the call duration?
Notes: * Delay
* Throughput
* Minimizing oscillations in encoding rate (stability)
* Reactivity to transient events
* Packet loss and discard rate
* Users' quality of experience

## Slide 4: Summary of Evaluation Guidelines
Avoiding Congestion Collapse
  Does it require any changes to circuit breakers?
Stability
  For stable link conditions does the sending rate oscillate, which may reduce the Quality of Experience
Media Traffic
  Variable motion, series of variable talk spurts
4-6. Diverse Environments
  Wired and wireless (802.11x, HSPA, GPRS)
  Varying Path Characteristics
  Reacting to Transient Events or Interruptions
Fairness With Similar Cross-Traffic
Impact on Cross-Traffic
Do we need a minimum set of guidelines?

## Slide 5: Evaluation Scenarios (1/4)
RTP on a fixed link
RTP
RTP
BW
For convenience we show only 3 hops and unidirectional flows

## Slide 6: Evaluation Scenarios (2/4)
RTP flow on a variable capacity link
RTP
RTP
BW

## Slide 7: Evaluation Scenarios (3/4)
Self-fairness
RTP
RTP
BW
RTP
RTP
…
…
These links can have same or different path properties

## Slide 8: Evaluation Scenarios (4/4)
Competing with TCP
  Short and long flows
  Small and large number of flows
RTP
RTP
RTP
RTP
…
…
TCP
TCP
…
TCP
TCP
…
BW

## Slide 9: Open Issues
Other metrics?
Clarify Topology: Dumbbell and Bus-stop
Clarify TCP and UDP flow parameters
Define simulation/emulation parameters
  Requirement document?
Notes: Duration of simulation
Packet and bit rates for CBR traffic
How to model TCP short flows