## Slide 1: Evaluating Congestion Control for Interactive Real-time Media
draft-singh-rmcat-cc-eval-02
11. March 2012
Varun Singh, Joerg Ott

## Slide 2: Current Status
02 version makes some changes based on input from last IETF
Main Open Issue: Metrics
  Discard Rate
    To measure trade-off of throughput and delay?
    Put in MAX ALLOWED END TO END DELAY
    Packets arriving later than this are DISCARDED
Notes: Quality per bit (PSNR, SSIM, visual comparison)

## Slide 3: Metrics
Bandwidth Utilization
  = RTP media rate/ bottleneck-link capacity
Packet loss and discard rate
Fair share with similar flows
  Media rate of all flows should be equal?
Fair share with TCP [remove it?]
  Last IETF: Comments on removing it
Notes: * Delay
* Throughput
* Minimizing oscillations in encoding rate (stability)
* Reactivity to transient events
* Packet loss and discard rate
* Users' quality of experience

## Slide 4: Summary of Evaluation Guidelines
Avoiding Congestion Collapse
  Does it require any changes to circuit breakers?
Stability
  For stable link conditions does the sending rate oscillate, which may reduce the Quality of Experience
Media Traffic
  Variable motion, series of variable talk spurts
4-6. Diverse Environments
  Wired and wireless (802.11x, HSPA, GPRS)
  Varying Path Characteristics
  Reacting to Transient Events or Interruptions
Fairness With Similar Cross-Traffic
Impact on Cross-Traffic [remove it?]
Do we need a minimum set of guidelines?

## Slide 5: Evaluation Scenarios
Video Start Rate: 128 kbps
Maximum end-to-end delay: 300ms
  200ms, 400ms?
  Different for audio and video?
Video Frame rate: 15
Audio packetization interval: 20ms
MTU: 1450 bytes

## Slide 6: Media
Use a packet generator
“varying amount of motion for video”
“variable frame size: I-frame, P-frame…”
Use real video streams
  http://media.xiph.org/video/derf/

## Slide 7: Topology
Dumbbell (common bottleneck link)
Parking lot (different bottleneck links)
RTP
RTP
RTP
RTP
RTP
RTP
RTP

## Slide 8: Evaluation Scenarios (1/4)
RTP on a fixed link
RTP
RTP
BW
For convenience we show only 3 hops and unidirectional flows

## Slide 9: Evaluation Scenarios (2/4)
RTP flow on a variable capacity link
RTP
RTP
BW
RTP
RTP
BW
BW
BW

## Slide 10: Evaluation Scenarios (3/4)
Self-fairness
RTP
RTP
BW
RTP
RTP
…
…
These links can have same or different path properties
Scenarios:
All start at same time
Media flows are added at intervals

## Slide 11: Open Issues
Other metrics?
  Trade-off between throughput, delay, loss
  Quality metric
Notes: Duration of simulation
Packet and bit rates for CBR traffic
How to model TCP short flows